## Slide 1
State of the Art in Imaging in Research and Development - Pharmacology
Mark E. Schmidt
Experimental Medicine

## Slide 2: Personal background
Graduate: MD University of Chicago 1983
Residency: General Psychiatry US Navy 1987
Fellowship Clinical Pharmacology NIMH 91-97
Clinical Research Physician Lilly Research Labs 97-2001
Senior Director Clinical Imaging Biomarkers Novartis AG 2001-2005
Senior Director Experimental Medicine Janssen NV 2005-present
  Neuroscience preclinical imaging team leader
  Preclinical DKI MRI IWT O&O investigator
  Clinical expert for PET imaging in Alzheimer’s disease
  Janssen liaison to the Alzheimer’s Disease Neuroimaging Initiative (ADNI)
  Clinical leader for early development of NMEs for the Mood and Alzheimer’s disease area strategies.

## Slide 3: Current collaborations and activities
PET radioligand discovery for neuroscience
  University of Leuven Laboratory of Radiopharmacy
PET imaging of translational models for Alzheimer’s disease
  University of Antwerp/Molecular Imaging Center Antwerp (MICA)
Innovatie door Wetteschap en Technologie (IWT) Onderzoek en Ontwikkeling (O&O)
  University of Antwerp Bioimaging Lab
    Diffusion kurtosis MRI in transgenic b-amyloid and tau pathology models
  University of Leuven Laboratory of Radiopharmacy
    Tau PET ligand
    Blood brain barrier and transporter function
Stellar
  Free University Amsterdam
    Tau PET (clinical)
ADNI PET Working Group

## Slide 4: Why Use Imaging as for Pharmaceutical Research and Development?
Can we detect? Expression of the target and/or activity of the pathway
Are we achieving? Potent target tissue exposure
Can we observe? Activity on the molecular target
Can we measure? Modulation of the desired biochemical pathway
Can we demonstrate? The desired biological effect
Does all this translate? To disease response
Paul Workman

## Slide 5: Performance Characteristics of Clinical Imaging Methods
Imaging Method | Temporal resolution | Spatial resolution | Sensitivity | Energy E=h
MEG | 1 msec | 5 mm |  | 
EEG | 1 msec | 10–15 mm |  | 
MRI | 100 msec single slice 3 sec multiple slice | 3.5 mm† 1-2 mm‡ | 10-5 molar | 107 Hz
PET | 45 sec* 20 min** | 6.5 mm* 4 mm** | 10-12 molar | 1017 Hz
SPECT | >60 sec | 6–8 mm | 10-12 molar | 1017 Hz
† GE BOLD 1.5T * H215O to measure CBF
‡ SE-BOLD 7T **18FDG to measure CMRglu
Adapted from: Farde, Rosen, Volkow PNAS 1997
Logothetis Nature 2008
5

## Slide 6: Why PET Imaging in CNS Drug Development?
The sensitivity of the method allows:
  Measurement and distribution of drug targets in vivo
  Measurement of drug compound in the target tissue in vivo
  Measurement of metabolic processes in vivo
Multiple isotopes allows:
  Range of time courses for measurement
  Flexibility in labeling small molecules and biologics
Readily translated from preclinical models to clinical application
  Serial assessments are possible: humans and preclinical species can serve as their own controls
An accessible technology for clinical trials:
  Hospital based
  Increasing availability through adoption of PET for diagnosis and treatment
  Increasing number of 18F labeled tracers
The challenge:
  Site specific tracers for new mechanisms of action may need to be developed

## Slide 7: Origins of CNS PET Radioligands Taken Into Human Subjects
V Pike NRM 2012

## Slide 8: Models for PET Ligand Development Used by Pharma
Ad hoc development of ligands with academic centers based on request by PET center, no collaboration
Radioligand candidate selection by clinical candidate project team, then external collaboration with PET center
Radioligand candidate development by internal chemistry group, in vivo testing done through contract or collaboration with PET center
Radioligand candidate development, in vivo testing in-house
Timeline
Intellectual property
Likelihood of technical success
Control over:
High
Low
Cost

## Slide 9: PET Ligand Development Process
PET First in Human
Clinical target portfolio entry
PET PoC
Discovery
Preclin. imaging
Quality control
PoC in HV
Beerse/Toledo/KUL
Clinical use
Beerse/KUL
Target selection and
initiation of project
Feasibility assessment
Tracer discovery
and characterisation
(chemistry,
pharmacology)
Initiated during HTL:
Allows the greatest diversity in chemical series, use of target screens and counterscreens
3H radiolabelling
PET radiolabelling
Ex vivo/in vivo distribution and competition
Kinetic modeling
Metabolism
Toxicology
Chem Pharm:
precursor synthesis, qualification of radiosynthesis
Registration dossier
PET used in
support of drug
development
(target distribution,
occupancy, PK,
efficacy)
Beerse/KUL
Beerse/KUL
Modeling and Analysis
Regulatory
Experimental Medicine/
Clin PK
PET NME Declaration

## Slide 10: Quantification of 18F-JNJ42259152, A Novel Phosphodiesterase-10A (PDE10A) PET-tracer : Kinetic Modeling and Test-Retest in Human Brain
K Van Laere 1, H Hudyana1, R Ahmad1, K Dubois2, M Schmidt2, G Bormans3 and M Koole1
1 Division of Nuclear Medicine, University Hospital Leuven, Belgium
2 Janssen Pharmaceutica R&D, Beerse, Belgium
3 Laboratory for Radiopharmacy, KU Leuven, Belgium
3
SNM Annual Meeting, Miami, Florida 2012

## Slide 11: Phosphodiesterase 10A (PDE10A)
Cyclic nucleotide phosphodiesterase superfamily
Dual substrate enzyme: hydrolization of cAMP & cGMP (Fujishige et al. 1999; Bender et al. 2006)
Coupled to D2 and D1 dopamine receptors
Restricted distribution in the human body (Seeger et al. 2003)
  - Brain : >> Striatum
  < Substantia Nigra
  << Nucleus Accumbens
  << Tuberculum olfactorium
Central role in striatal (cAMP/PKA) signaling : cAMP activates PKA which is responsible for phosphorylation of various intracellular targets (eg. DARPP-32) altering cellular function (Surmeier et al. 2007)
Implicated in several neuropsychiatric disorders
  Schizophrenia (Siuciak et al, 2006), movement disorders (Huntington’s disease) (Hebb et al, 2004), addiction (Menniti et al, 2006)
  Treatment potential of PDE10A inhibitors

## Slide 12: PET tracers for PDE10A
2-[[4-[1-(2-[18F]fluoroethyl)-4-(4-pyridinyl)-1H-pyrazol-3-yl]phenoxy]methyl]-3,5-dimethyl-pyridine
MW=401.46
Affinity : pIC50=8.79 ± .01
Selectivity for PDE10A: 1000-fold over other PDE subtypes, no other targets below mM level
Plasma protein binding ≈ 99.5 %
18F-JNJ42259152
  Previous ligands ?
    11C-papaverine (Tu et al. 2010): rapid washout from CNS
    11C-MP10 (Tu et al. 2011): BBB penetrable radiometabolite

## Slide 13: [18F]-JNJ42259152: PET Ligand for PDE10
Chart: Time p.i. (s)
| 7.5 | 22.5 | 37.5 | 52.5 | 90 | 150 | 210 | 270 | 390 | 570 | 750 | 930 | 1110 | 1350 | 1650 | 1950 | 2250 | 2550 | 2850 | 3150 | 3450 | 3780 | 4140 | 4500 | 4860 | 5220 | 5580 | 5940 | 6300 | 6660 | 7020
striatum | 0.29206 | 0.67823 | 0.71629 | 0.70887 | 0.74619 | 0.72303 | 0.7225 | 0.76506 | 0.76861 | 0.76261 | 0.78045 | 0.76528 | 0.7449 | 0.77012 | 0.7267 | 0.71832 | 0.69053 | 0.65862 | 0.64569 | 0.6031 | 0.57986 | 0.56175 | 0.53019 | 0.52385 | 0.4854 | 0.47436 | 0.45544 | 0.44336 | 0.44047 | 0.40452 | 0.38078
cortex | 0.37136 | 0.75656 | 0.68941 | 0.7078 | 0.62392 | 0.54614 | 0.49217 | 0.46908 | 0.42674 | 0.39726 | 0.38703 | 0.36047 | 0.35159 | 0.34758 | 0.34302 | 0.33622 | 0.34001 | 0.33646 | 0.34223 | 0.33836 | 0.3438 | 0.3405 | 0.34639 | 0.35387 | 0.34997 | 0.34555 | 0.34364 | 0.34995 | 0.3501 | 0.34979 | 0.35484
CBL | 0.44534 | 0.96689 | 0.85543 | 0.89822 | 0.77703 | 0.49489 | 0.4848 | 0.50119 | 0.34409 | 0.31313 | 0.28254 | 0.27858 | 0.25737 | 0.23285 | 0.24026 | 0.22647 | 0.24754 | 0.27245 | 0.24832 | 0.24208 | 0.25883 | 0.26771 | 0.27097 | 0.27162 | 0.27255 | 0.27971 | 0.2823 | 0.28768 | 0.28641 | 0.22841 | 0.28843
striatum | 0.25534 | 0.71794 | 0.75789 | 0.90477 | 0.80234 | 0.78227 | 0.78519 | 0.73188 | 0.69384 | 0.68934 | 0.69468 | 0.70818 | 0.7224 | 0.73486 | 0.73188 | 0.60098 | 0.46447 | 0.37153 | 0.34709 | 0.32084 | 0.31213 | 0.30362 | 0.26508 | 0.24463 | 0.23874 | 0.24219 | 0.24874 | 0.24896 | 0.23263 | 0.24497 | 0.21932
cortex | 0.37915 | 0.76886 | 0.75875 | 0.7222 | 0.64135 | 0.54055 | 0.46295 | 0.423 | 0.36716 | 0.32788 | 0.30535 | 0.31083 | 0.29688 | 0.29267 | 0.30043 | 0.28416 | 0.25176 | 0.24428 | 0.25183 | 0.24598 | 0.25327 | 0.25104 | 0.25794 | 0.26249 | 0.27052 | 0.27501 | 0.28385 | 0.28469 | 0.28756 | 0.29724 | 0.30046
CBL | 0.36732 | 0.98393 | 0.93184 | 0.96784 | 0.75013 | 0.58741 | 0.47099 | 0.35036 | 0.26993 | 0.26349 | 0.23059 | 0.21915 | 0.21038 | 0.21329 | 0.18804 | 0.19313 | 0.2242 | 0.20951 | 0.228 | 0.21646 | 0.21781 | 0.2251 | 0.21858 | 0.21738 | 0.20214 | 0.23381 | 0.21956 | 0.20903 | 0.23496 | 0.23076 | 0.22653
Before chase JNJ302 (10 mg/kg)
After chase JNJ302 (10 mg/kg)
Complete displacement of PET ligand [18F]JNJ152 after administration of
JNJ302 (2.5 mg/kg i.v. chase)
Vehicle or
JNJ302 (2.5 mg/kg, i.v.)
Chase
JNJ302
2.5 mg/kg
Chase
vehicle
Notes: M0005176: F18-JNJ152: Chase studie met JNJ302 30 min post tracer injectie , iv, dosis 0; 2.5;10 mg/kg n=3 (isoflurane)
Dynamisch 120 min
M0005176 /
F18-JNJ152
Gewicht (g)
Inj dosis (mCi)
Vervolg
Rat 1 nieuwe jonge
292
1,88
OK
Rat 2 nieuwe jonge
284
1,86
OK
Rat 3 nieuwe jonge
296
1,74
OK

## Slide 14
Results in Human
Chart: Time PI (sec)
| 7.5 | 22.5 | 37.5 | 52.5 | 90 | 150 | 210 | 270 | 375 | 525 | 750 | 1050 | 1350 | 1650 | 1950 | 2250 | 2550 | 2850 | 3150 | 3450 | 3750 | 4050 | 4350 | 4650 | 4950 | 5249.5 | 6451 | 6751 | 7051 | 7351 | 7651 | 7951
putamen | 0.27457 | 1.9018 | 1.625 | 1.8266 | 2.0022 | 1.9803 | 2.0634 | 2.2917 | 2.5098 | 2.5745 | 2.6449 | 2.5453 | 2.4775 | 2.3473 | 2.2451 | 2.1272 | 2.0164 | 1.9266 | 1.8427 | 1.8157 | 1.699 | 1.6318 | 1.5499 | 1.5738 | 1.4694 | 1.4244 | 1.1937 | 1.2335 | 1.1393 | 1.0738 | 1.0545 | 1.0646
caudate_nucleus | 0.24299 | 1.8243 | 1.3457 | 1.4112 | 1.6386 | 1.5773 | 1.6998 | 1.7476 | 1.9393 | 1.994 | 2.0181 | 1.8865 | 1.7838 | 1.7167 | 1.5143 | 1.4668 | 1.3617 | 1.2457 | 1.1978 | 1.0968 | 1.0051 | 1.0176 | 0.9328 | 0.86952 | 0.84727 | 0.77571 | 0.72406 | 0.65818 | 0.65465 | 0.6451 | 0.59194 | 0.63159
ventral_striatum | 0.32234 | 2.4384 | 1.7495 | 1.2254 | 1.6334 | 1.6846 | 1.8518 | 1.7715 | 1.8425 | 1.7891 | 1.8109 | 1.6968 | 1.5272 | 1.4035 | 1.3037 | 1.1774 | 1.101 | 0.98854 | 0.92786 | 0.82303 | 0.76189 | 0.75691 | 0.72635 | 0.68384 | 0.67939 | 0.59989 | 0.55712 | 0.53079 | 0.50461 | 0.47684 | 0.51047 | 0.46348
substantia_nigra | 0.27633 | 3.0714 | 1.2416 | 1.4896 | 1.2889 | 1.2126 | 1.0574 | 1.1504 | 1.1423 | 1.1655 | 1.0882 | 0.95722 | 0.8719 | 0.79452 | 0.70401 | 0.66929 | 0.66246 | 0.57571 | 0.62024 | 0.52995 | 0.51404 | 0.46459 | 0.45345 | 0.38133 | 0.4497 | 0.38263 | 0.36508 | 0.36871 | 0.35772 | 0.27543 | 0.38078 | 0.29102
thalamus | 0.24734 | 1.9968 | 1.6965 | 1.7589 | 1.4274 | 1.3477 | 1.351 | 1.2743 | 1.2391 | 1.1258 | 0.9336 | 0.75934 | 0.62785 | 0.58422 | 0.516 | 0.4674 | 0.43604 | 0.3787 | 0.38941 | 0.36397 | 0.35241 | 0.33587 | 0.31151 | 0.31274 | 0.29873 | 0.26988 | 0.27896 | 0.26603 | 0.23764 | 0.24672 | 0.24599 | 0.23577
frontal_cortex | 0.21453 | 2.0069 | 1.5084 | 1.441 | 1.4213 | 1.2504 | 1.1402 | 1.0854 | 1.0399 | 0.90224 | 0.76515 | 0.62231 | 0.52361 | 0.47528 | 0.42581 | 0.39119 | 0.37209 | 0.34279 | 0.33081 | 0.32877 | 0.31846 | 0.30544 | 0.28323 | 0.29285 | 0.28264 | 0.27115 | 0.26117 | 0.24955 | 0.24733 | 0.25407 | 0.24259 | 0.23606
cerebellum | 0.34149 | 2.1095 | 1.8986 | 1.8644 | 1.655 | 1.569 | 1.4194 | 1.4127 | 1.3149 | 1.1617 | 0.96968 | 0.76037 | 0.59489 | 0.51881 | 0.46425 | 0.4258 | 0.39184 | 0.34818 | 0.3325 | 0.31494 | 0.30726 | 0.28419 | 0.28688 | 0.26711 | 0.27593 | 0.26248 | 0.23827 | 0.22674 | 0.22727 | 0.23808 | 0.22804 | 0.21986
white matter | 0.19555 | 0.98503 | 0.70967 | 0.5977 | 0.61062 | 0.55205 | 0.63452 | 0.6684 | 0.54697 | 0.55652 | 0.51954 | 0.53789 | 0.56833 | 0.50884 | 0.46345 | 0.42437 | 0.43694 | 0.37323 | 0.37168 | 0.3516 | 0.3085 | 0.33046 | 0.27911 | 0.30216 | 0.27285 | 0.26294 | 0.21832 | 0.20256 | 0.20196 | 0.22659 | 0.21161 | 0.16405

## Slide 15
PiB PET as Treatment Endpoint in Clinical Trials of
anti-Aβ MABs
A
A
-
0.09
-
0.09
A
A
A
A
Screen
Week 78
B
B
-
0.33
-
0.33
B
B
B
B
Screen
Week 78
Rinne et al, Lancet Neurology 2010
Bapineuzumab (n=19)
Placebo (n=7)
Ostrowitzki et al, Arch Neurol 2011
Gantenerumab (n=6/6)
Placebo (n=4)
Notes: 15
As recently published in Lancet Neurology, using PIB PET technology, bapineuzumab treatment has been shown to reduce beta amyloid in people with mild to moderate AD.
Panels A and B show 2 different AD patients who were treated with bapineuzumab. Each panel shows the amount of brain amyloid as detected by PIB PET before initiating treatment and also at Wk78 after 18 months of treatment. There is reduction in brain amylolid both subjects after bapineuzumab treatment as detected by PIB PET.
The graph in the right hand panel shows the increasing amyloid reduction over time with bapineuzumab treatment (in red) and increase in amyloid burden in placebo treated AD subjects (in blue).
So this was very important research, part of a larger puzzle – which we’re continuing to put together piece by piece.
And that brings us to the new data that we’re presenting today.

## Slide 16: 11C-PiB SUVR as a Longitudinal Measure: How well does it scale in multi-site trials?
Some subjects show trajectories not consistent with biological change and in excess of test-retest variability
Data from ADNI http://www.adni-info.org/